Wiring Instructions

# Passenger Side

Tan/White (Low Beam) –Blue Wire (2)

Yellow/White (High Beam)-Yellow Wire (1)

Brown (Ground) –Black (4)

- Green Wire is for city light bulb in the head lamp T-Tap to parking lamp wire or cut and butt connect .

# Drivers Side

White/Black (low Beam) – Blue Wire (2)

Yellow/Black (High Beam)-Yellow Wire (1)

Brown (Ground)-Black (4)

- Green Wire is for city light bulb in the head lamp T-Tap to parking lamp wire or cut and butt connect .

- Remove corner lamp see Owners manual

- Cut edge of the fender see picture

- Disconnect Battery

- Unplug Headlamp , roll back rubber boot and push metal clip down and pull back

- Remove Headlamp (3)  Torx Screw T-30 Two on top and one on the side

- Remove Headlamp by sliding out  toward corner area  and the wiggle out

- Look at plug  locate purple triangular part  move up. Slide off  Plastic housing

- There should be 4 wires 3 large and 1 small.

- Slide Heat shrink over the 3 larger wires

- Plug in wires according to chart above Slide  Heat shrink over wire

**Before Shrinking plug on headlamp reconnect battery and check functions High low**

- Next Shrink tubing using lighter, Slide over Bigger heat shrink to seal the three wires

- Install Headlamp ,Install the headlamp pivot point into the hole ,  Insert two top torx screws

- Plug Harness on headlamps