# Technical Data – Audi TT Coupé 2.0 TFSI

Programme for Germany – Status: April 2006

| Model | Audi TT Coupé 2.0 TFSI |
| --- | --- |
| Engine / electrics |  |  |  |  |
| Engine type | Inline four-cylinder spark-ignition engine with petrol direct injection, exhaust turbo-charger with intercooler, 4 valves per cylinder, double overhead camshafts (DOHC) |
| Valve gear / number of valves per cylinder | Continuous intake camshaft adjustment |
| Displacement in cc / bore x stroke in mm / compression | 1984 / 82.5 x 92.8 / 10.3 |
| Max. power output in kW (bhp) / at rpm | 147 (200) / 5100 - 6000 |
| Max. torque in Nm / at rpm | 280 / 1800 - 5000 |
| Engine management / mixture preparation | Fully electronic engine management with drive-by-wire throttle control, direct injection, adaptive lambda control; mapped ignition with solid-state high-voltage distribution, cylinder-selective adaptive knock control |
| Exhaust emission control | Close-coupled ceramic primary catalytic converter with catalyst heating function via homogeneous split dual injection |
| Emission category | EU 4 |
| Alternator in A / battery in A/Ah | 140 / 330/61 |
| Drive / transmission |  |  |  |  |
| Drive type | Front-wheel drive |
| Clutch | Hydraulically operated single-plate dry clutch with asbestos-free and lead-free linings | Two electro-hydraulically controlled multi-plate clutches in an oil bath |
| Gearbox type | 6-speed manual gearbox, synchromesh on all gears | 6-speed dual-clutch gearbox S tronic with electro-hydraulic control |
| Gear ratio in 1st gear / 2nd gear | 3.357 / 2.087 | 3.462 / 2.150 |
| Gear ratio in 3rd gear / 4th gear | 1.469 / 1.150 | 1.464 / 1.079 |
| Gear ratio in 5th gear / 6th gear | 1.194 / 0.975 | 1.094 / 0.921 |
| Gear ratio in reverse gear | 3.990 | 3.989 |
| Final drive ratio in 1st - 4th gear / 5th, 6th and reverse gear | 3.944 / 3.087 | 4.059 / 3.136 |
| Running gear / steering / brakes |  |  |  |  |
| Front suspension | McPherson struts with aluminium lower wishbones, aluminium pivot bearings, aluminium subframe, anti-roll bar, track-stabilising steering roll radius |
|  | Four-link rear suspension with separate spring/shock absorber arrangement, subframe, tubular anti-roll bar |
| Steering / steering ratio / turning circle in m (D102) | Electromechanical steering with speed-dependent power assistance; steering wheel turn lock to lock: 2.9 Steering ratio: 16.9; Turning circle (D102): 10.96 |
| Brake system, front/rear | Dual-circuit brake system with diagonal split, ESP, hydraulic brake assist, disc brakes ventilated at front, solid at rear Brake system: 16“/16“; brake diameter front/rear: 312 / 286 |
| Wheels / tyres | Wheels: weight-optimised aluminium 7.5Jx16, offset: 45; tyres: 225/55 R16 95W |
| Performance / consumption / acoustics |  |  |  |  |
| Maximum speed in km/h | 240 | 240 |
| Acceleration, 0-100 km/h in seconds | 6.6 | 6.4 |
| Fuel grade | Super Plus unleaded, 98 RON |
| Fuel consumption: urban / extra urban / overall, l/100 km | 10.7 / 6.0 / 7.7 | 10.6 / 6.0 / 7.7 |
| CO2 overall mass emissions, g/km | 183 | 183 |
| Standing / drive-past exterior noise level in dB (A) | 87 / 75 | 87 / 74 |
| Servicing / guarantee (Germany) |  |  |  |  |
| Oil change every ... km / inspection every ... km | Nach Serviceanzeige bis 30.000 (max. 2 Jahre) 1) |
| Vehicle/paint/rust perforation guarantee | 2 years with unlimited mileage / 3 years / 12 years |
| Insurance classification: third party / fully comprehensive / part-comprehensive | Data not available at time of printing |
| Weights / loads |  |  |  |  |
| Unladen weight (excl. driver) / gross weight limit in kg | 1260 / 1660 | 1280 / 1680 |
| Axle load limit at front / rear in kg | 945 / 785 | 965 / 785 |
| Trailer load limit unbraked in kg | - |
| Trailer load limit on 8% / 12% gradient, braked in kg | - / - |
| Roof load limit in kg | Data not available at time of printing |
| Capacities |  |  |  |  |
| Cooling system capacity (incl. heating) in l | 9.0 |
| Engine oil capacity (incl. filter) in l | 4.6 |
| Fuel tank capacity in l | 55 |
| Body / dimensions |  |  |  |  |
| Body type | Audi Space Frame (ASF) |
| Number of seats | 2 + 2 |
| Drag coefficient cD / frontal area A in m2 | 0.30 / 2.09 |
| Length (L103) / width excl. mirrors (W103) /height (H100),mm | 4178 / 1842 / 1352 |
| Wheelbase (L101) / track at front/rear (W101/W102), mm | 2468 / 1572 / 1558 |
| Height of loading lip in mm (H196) | 790 |
| Luggage capacity in l, acc. to VDA block method (V210) | 290 (700 with rear seat folded down) |

- depending on driving style and operating conditions			provisional figures