TCM Reset Instructions

There will be errors present in the transmission control module as a result of the flashing process.

There are two ways to clear these errors in the module before proceeding with the transmission adaptation reset.

- If you have a scan tool like VCDS (vag-com) or OBD11 you can go into the (02) transmission control module. Then go into read DTC’s, and then click on clear DTC’s

- If you do not have a scan tool, please install the module and THEN disconnect the negative terminal of the battery for 5-10 minutes. The negative terminal is located under the driver floor mat underneath of a small plastic access cover. Once the time has passed please reconnect the negative terminal.

Now that they error codes have been erased, you may proceed with the “nooby” transmission adaptation reset. This is done by having the key on, but engine off. Next press the accelerator pedal to the floor for 15 seconds. Now turn the key off, and then drive as you normally would.