# Technical Data – Audi TT Coupé 3.2 quattro

Programme for Germany – Status: April 2006

| Model | Audi TT Coupé 3.2 quattro |
| --- | --- |
| Engine / electrics |  |  |  |  |
| Engine type | Six-cylinder spark-ignition engine, DOHC |
| Valve gear / number of valves per cylinder | Roller cam followers / 4 |
| Displacement in cc / bore x stroke in mm / compression | 3189 / 84.0 x 95.9 / 11.3 |
| Max. power output in kW (bhp) / at rpm | 184 (250) / 6300 |
| Max. torque in Nm / at rpm | 320 / 2500 -3000 |
| Engine management / mixture preparation | Motronic ME 7.1.1: fully electronic sequential injection, overrun fuel cut-off, adaptive lambda control; mapped ignition with solid-state high-voltage distribution; cylinder-selective adaptive knock control, air-mass measurement; coordinated torque control; intake and exhaust camshaft adjustment; secondary air injection |
| Exhaust emission control | 4 oxygen sensors (2 heated), activated carbon filter, 3-way catalytic converter |
| Emission category | EU 4 |
| Alternator in A / battery in A/Ah | 140 / 380/72 |
| Drive / transmission |  |  |  |  |
| Drive type | quattro permanent four-wheel drive with electronically controlled multi-plate clutch, electronic differential lock EDL |
| Clutch | Hydraulically operated single-plate dry clutch with asbestos-free and lead-free linings | Two electro-hydraulically controlled multi-plate clutches in an oil bath |
| Gearbox type | 6-speed manual gearbox, synchromesh on all gears | 6-speed dual-clutch gearbox S tronic with electro-hydraulic control |
| Gear ratio in 1st gear / 2nd gear | 3.357 / 2.087 | 2.933 / 1.833 |
| Gear ratio in 3rd gear / 4th gear | 1.469 / 1.088 | 1.300 / 0.975 |
| Gear ratio in 5th gear / 6th gear | 1.108 / 0.912 | 1.030 / 0.825 |
| Gear ratio in reverse gear | 3.990 | 3.35 |
| Final drive ratio in 1st - 4th gear / 5th, 6th and reverse gear | 4.235 / 3.273 | 4.800 / 3.600 |
| Running gear / steering / brakes |  |  |  |  |
| Front suspension | McPherson struts with aluminium lower wishbones, aluminium pivot bearings, aluminium subframe, anti-roll bar, track-stabilising steering roll radius |
| Rear suspension | Four-link rear suspension with separate spring/shock absorber arrangement, aluminium subframe, tubular anti-roll bar |
| Steering / steering ratio / turning circle in m (D102) | Electromechanical steering with speed-dependent power assistance; steering wheel turn lock to lock: 2.9 Steering ratio: 16.9; Turning circle (D102): 10.96 |
| Brake system, front/rear | Dual-circuit brake system with diagonal split, ESP, hydraulic brake assist, disc brakes, ventilated at front and rear Brake system: 17“/17“; brake diameter front/rear: 340 / 310 |
| Wheels / tyres | Wheels: lightweight forged aluminium 8.5Jx17, offset: 50; tyres: 245/45 R17 95Y |
| Performance / consumption / acoustics |  |  |  |  |
| Maximum speed in km/h | 250 (governed) | 250 (governed) |
| Acceleration, 0-100 km/h in seconds | 5.9 | 5.7 |
| Fuel grade | Super Plus unleaded, 98 RON |
| Fuel consumption: urban / extra urban / overall, l/100 km | 14.7 / 7.8 / 10.3 | 12.9 / 7.3 / 9.4 |
| CO2 overall mass emissions, g/km | 247 | 224 |
| Standing / drive-past exterior noise level in dB (A) | 81 / 75 | 81 / 73 |
| Servicing / guarantee (Germany) |  |  |  |  |
| Oil change every ... km / inspection every ... km | According to service indicator up to 30,000 (max. 2 years) 1) |
| Vehicle/paint/rust perforation guarantee | 2 years with unlimited mileage / 3 years / 12 years |
| Insurance classification: third party / fully comprehensive / part-comprehensive | Data not available at time of printing |
| Weights / loads |  |  |  |  |
| Unladen weight in kg (excl. driver) / gross weight limit; kg | 1410 / 1810 | 1430 / 1830 |
| Axle load limit at front / rear in kg | 1015 / 870 | 1035 / 870 |
| Trailer load limit unbraked in kg | - |
| Trailer load limit on 8% / 12% gradient, braked in kg | - / - |
| Roof load limit in kg | Data not available at time of printing |
| Capacities |  |  |  |  |
| Cooling system capacity (incl. heating) in l | 12.7 l |
| Engine oil capacity (incl. filter) in l | 5.5 |
| Fuel tank capacity in l | 60 |
| Body / dimensions |  |  |  |  |
| Body type | Audi Space Frame (ASF) |
| Number of seats | 2 + 2 |
| Drag coefficient cD / frontal area A in m2 | 0.31 / 2.09 | 0.30 / 2.09 |
| Length (L103) / width excl. mirrors (W103) /height (H100),mm | 4178 / 1842 / 1352 |
| Wheelbase (L101) / track at front/rear (W101/W102), mm | 2468 / 1572 / 1558 |
| Height of loading lip in mm (H196) | 790 |
| Luggage capacity in l, acc. to VDA block method (V210) | 290 (700 with rear seat folded down) |

- depending on driving style and operating conditions